Dynamic LPAR Tips/Checklist
for RMC Authentication and Authorization

Version: 0.4

Printed on March 4, 2003

This document was last updated on 11/01/2002

Please direct comments to Truc D. Nguyen

truc@us.ibm.com

| The information contained in this document has not been submitted to any formal IBM test and is distributed as is. The use of this information or the implementation of any of these techniques is the implementors responsibility and depends on the implementors ability to evaluate and integrate them into the customers operational environment. The customer must be made aware of all actions that will result in a permanent change to their environment While each item may have been reviewed by IBM for accuracy in a specific situation, there in no guarantee that the same or similar results will be obtained elsewhere. Individuals attempting to adapt these techniques to a specific customer environment do so at their own risk. This copy of the document may be obsolete. The user should obtain an updated copy from the website: http://w3.austin.ibm.com/:/projects/yxia/ |
| --- |
| 1.0 Verify the DLPAR Requirements | 4 |
| 2.0 Checklist for DLPAR Setup | 4 |
| 2.1 Verify If the Required Software is Functional | 4 |
| 2.2 Verify Your RMC/DLPAR Network/Hostname Setup | 6 |
| 3.0 Setting up the HMC/Partition(s) Hostname and Network | 7 |
| 3.1 If DNS is On | 8 |
| 3.1.1 If the HMC and the Partition(s) both use Long name | 8 |
| 3.1.2 Other Hostname Formats | 8 |
| 3.2 If DNS is Off | 8 |
| 4.0 Procedures for Renaming a HMC/Partition Hostname, Redefining a Partition, orSwitching a Partition between SMP and LPAR Mode | 9 |
| 4.1 Step 1: Removing IBM.ManagedNode Resources on HMC | 9 |
| 4.2 Step 2: Removing IBM.ManagementServer Resource on Partitions | 9 |
| 5.0 Appendix 1: Other Useful Tips/Checks | 11 |
| 5.1 To access Linux on the HMC | 11 |
| 5.2 An Alternate Way to Open an Xterm on HMC | 11 |
| 5.3 Use LAN Surveillance to Check Your Network Problem | 11 |
| 5.4 An Quick Way to Verify if the System Network/Hostname is set up Properly | 12 |
| 5.5 Check Serial Cable Connection Between HMC and CEC | 12 |
| 5.6 Checking for HMC version from ssh | 12 |
| 6.0 Appendix 2: Common Questions for RMC/DLPAR | 13 |
| 6.1 Is There a Relation b/w DLPAR/LparCmdRM and SFP/ServiceRM? | 13 |
| 6.2 Authentication & Authorization Process between HMC & Partitions | 13 |
| 6.3 What Does the Output of lspartition -dlpar Mean? | 14 |
| 6.4 Do IBM.DRM and IBM.HostRM Need to be “Active” on Partition for DLPAR to Work? | 14 |
| 6.5 Does IBM.CSMAgentRM Need to be Active on HMC? | 14 |
| 7.0 Appendix 3: Known Defects with HMC GA3 GOLD | 15 |
| 7.1 Problem #1: HMC’s acls File is Missing the DEFAULT Stanza | 15 |
| 7.2 Problem #2: Lspartition -dlpar Shows Active <1> but the DLPAR is not Enabled on the GUI | 15 |
| 7.3 Problem #3: AIX ctcas daemon is ‘inoperative’ on AIX | 15 |
| 7.4 Problem #4: AIX ctcas daemon is ‘inoperative’ on HMC | 16 |
| 7.5 Program #5: IBM.DMSRM hangs on HMC | 16 |
| 8.0 Change History | 17 |
| 9.0 References | 18 |

Verify the DLPAR Requirements

Please see Appendix section for instruction how to access Linux on command line.

|  | Verify | > Command -> Result -> Action |
| --- | --- | --- |
| 1 | HMC level |

Click [Help] and then [About] on the HMC main window.

This should be release 3 version 1.1 or  higher

Customers are encouraged to get the latest software which can be obtained at

http://techsupport.services.ibm.com/server/hmc?fetch=corrsrv.html

2

AIX Firmware

> lsmcode

Platform Firmware level is RKA20905

System Firmware level is RG02*_GA3_*

3

AIX filesets required for  DLPAR

(on each LPAR/SMP)

AIX level should 5.2. These following filesets should be on partitions.

> lslpp -l rsct.core* 
> lslpp -l csm.client

The missing fileset can be installed from the AIX installation CD.

Checklist for DLPAR Setup

Verify If the Required Software is Functional

|  | Verify | Result and Action |
| --- | --- | --- |
| 1 | HMC daemons are running |

> su - root
> lssrc -a

Subsystem         Group         PID     Status
 ctrmc            rsct          822     active
 ctcas            rsct          823     active
 IBM.DMSRM        rsct_rm       906     active
 IBM.LparCmdRM    rsct_rm       901     active

If these daemons are active go to step 2:

If any of the daemons show as inoperative, start it manually by

> startsrc -s <subsystem name>

Example: startsrc -s ctcas

If  a daemon can't be started

Please contact IBM service personnel.

2

AIX daemons are running

(on each LPAR/SMP with AIX 5.20)

> su - root
> lssrc -a | grep rsct

Subsystem         Group         PID      Status
 ctrmc            rsct          21044    active
 ctcas            rsct          21045    active
 IBM.CSMAgentRM   rsct_rm       21045    active
 IBM.ServiceRM    rsct_rm       11836    active
 IBM.DRM          rsct_rm       20011    active
 IBM.HostRM       rsct_rm       20012    active

IBM.DRM and IBM.HostRM are ‘lazy started’ resource managers which means they’re only started when they get used. If IBM.DRM and IBM.HostRM are "inoperative,” there is a good chance that you’re having network/hostname setup problem between HMC and the partition; to correct this, please refer to section “Verify Your  RMC/DLPAR Setup.”

If any of the daemons show as inoperative

> startsrc -s <subsystem name>

Example: startsrc -s ctcas

If ctcas can’t be started

If ctcas can't be started, please open a PMR before contact your IBM service personnel.

NOTES:

ctrmc: is a RMC subsystem
ctcas: is for security verification
IBM.DMSRM: is for tracking statuses of partitions
IBM.LparCmdRM: is for DLPAR operation on HMC
IBM.CSMAgentRM: is for  handshaking between the partition and HMC
IBM.DRM: is for executing the DLPAR command on the partition.
IBM.HostRM: is for obtaining OS information.

Verify Your RMC/DLPAR Network/Hostname Setup

|  | Verify | >Result and Actions |
| --- | --- | --- |
| 1 |

HMC: List partitions authenticated  by RMC

> /opt/csm/bin/lsnodes -a Status

partition01    1
partition02    0
partition03    1

Where “1” means partition is activated and authenticated for DLPAR; “0” means otherwise.

| If the partition is activated and still shows Active<0>, you could either have network or hostname setup problem. If you have just rebooted the HMC, wait for a few minutes. If nothing changes after that, check your hostname/network setup as in section Setting up HMC /Partition(s) Hostname and Network. |
| --- |
| 2 | HMC: List partitions recognized by DLPAR |

> lspartition -dlpar

<#0> Partition:<001, partition01.company.com, 9.3.206.300> Active:<1>, OS:<AIX, 5.2>, DCaps:<0xf>, CmdCaps:<0x1, 0x0>

<#1> Partition:<002, partition02.company.com, 9.3.206.300> Active:<0>, OS:<AIX, 5.2>, DCaps:<0xf>, CmdCaps:<0x1, 0x0>

<#2> Partition:<003, partition03.company.com, 9.3.206.300> Active:<0>, OS:<, 5.1F>, DCaps:<0x0>, CmdCaps:<0x0, 0x0>

If all active AIX 5.2 partitions are listed as Active<1>, ..., DCaps:<0xf> your system has been set up properly for DLPAR, you can skip the checklist now.

(In this example, partition 002 is being shut down, partition 003 is not activated for it is AIX 5.1.)

If you’re missing some active partitions or some partitions are reported as Active<0>, your system probably still has network/hostname set up problem. Refer to section Setting up  HMC/Partition(s) Hostname and Network.

(If you partition is Active<1> but the GUI is still not DLPAR capable, do a rebuild to get around this problem. See Appendix session for more information about this problem.)

If you still can’t get partitions recognized by DLPAR after verifying the checklist, contact IBM service personnel.

3

AIX: Ensure   /var directory is not 100% full

(on each LPAR/SMP)

> df

If  /var  is 100% full, use smitty to expand it. If there is no more space available, visit subdirectories to remove unnecessary files (e.g. trace.*, core, etc.)

After expanding the /var directory, execute these command to fix possibly corrupted files.

> rmrsrc -s "Hostname!='t' " IBM.ManagementServer > /usr/sbin/rsct/bin/rmcctrl -z > rm /var/ct/cfg/ct_has.thl > rm /var/ct/cfg/ctrmc.acls > /usr/sbin/rsct/bin/rmcctrl -A

4

AIX: Verify if you have network problem?

(From each LPAR/SMP)

> ping <hmc_hostname>

If ping fails, check your hostname/network setup. See section Setting up HMC/Partition(s) Hostname and Network.

5

AIX: Verify partition(s) to HMC authentication

(from each LPAR/SMP)

> CT_CONTACT=<HMC name> lsrsrc IBM.ManagedNode

You should get a list of resource classes on HMC.

| If there is any error, you probably have network/hostname problem, please refer to section Setting up HMC /Partition(s) Hostname and Network. |
| --- |
| 6 | HMC: Verify network setup by telnet-ing into each partition(s) from the HMC. |

> telnet <hostname>

> "Ctrl c" or "exit" to end

| If you can’t telnet, you have a network problem, refer to section 3.0 Setting up HMC/Partition(s) Hostname and Network. |
| --- |
| 7 | HMC: Verify HMC to partition(s) authentication |

> CT_CONTACT =<partition_hostname> lsrsrc IBM.ManagementServer

If nothing is displayed or if there are any errors, you probably have a hostname problem, please refer to section Setting up HMC /Partition(s) Hostname and Network.

Setting up the HMC/Partition(s) Hostname and Network

Most of DLPAR problems we have encounter from the labs during testing have been improper network and hostname(s) setup. This section aims to reduce these network setup/configuration problems.

First, find out the hostname format the HMC and its partition(s) are using; short or long name. Your setup depends largely on the format of the hostname. The hostname format can be determined by typing the command "hostname” on the HMC and AIX system respectively then use “host return_from_hostname” to verify it.

Example:

> hostname

Partition.company.com

> host Partition.company.com

Partitition.company.com has address 9.3.14.199

If DNS is On

If the HMC and the Partition(s) both use Long name

No hostname entry is needed in /etc/hosts on either AIX or the HMC.

If /etc/hosts has the hostname entry, the longname must be before the short name for HMC and all partitions (host names are case sensitive).

Example:

10.10.10.11    mymachine.mycompany.com      mymachine

After update /etc/host file, refresh RMC by either rebooting or

> /usr/sbin/rsct/bin/rmcctrl -z
  > /usr/sbin/rsct/bin/rmcctrl -A

Other Hostname Formats

If the hostname command returns the short name, put the shortname before the longname in /etc/hosts on both HMC and the partitions; If the hostname command returns the long name, put the longname before the shortname in the /etc/hosts file on HMC and all partitions (names are case sensitive).

Example:

10.10.10.11    mymachine      mymachine.mycompany.com

Make sure that on the partition(s) (just partition(s)), the file /etc/netsvc.conf exists with one line:  hosts=local,bind

Refresh RMC by either rebooting or by commands

> /usr/sbin/rsct/bin/rmcctrl -z

> /usr/sbin/rsct/bin/rmcctrl -A

If DNS is Off

The HMC and partition(s) /etc/hosts file need to be modified to contain the correct entries for the HMC and all partitions’ hostnames. If the hostname command returns the short name, put the short name before the longname in /etc/hosts for HMC and all partitions (names are case sensitive). If the hostname command returns the long name, put the long name before the short name in /etc/hosts for HMC and all partitions (names are case sensitive)

Make sure that on the partition(s) (just partition), file /etc/netsvc.conf exists with one line:  hosts=local,bind.

Refresh RMC by either rebooting or

> /usr/sbin/rsct/bin/rmcctrl -z
  > /usr/sbin/rsct/bin/rmcctrl -A

Customers should add all the LPAR's hostnames to the /etc/hosts file on the HMC. The HMC hostname must be added to each LPAR /etc/hosts file. Because the customer does not have DNS data, we do not have a domain name, only a short hostname, therefore the DNS enabled box will not  be enabled.

Procedures for 
Renaming a HMC/Partition Hostname, 
Redefining  a Partition, or
Switching a Partition between SMP and LPAR Mode

NOTE: This procedure is required only if you have the HMC GA3 GOLD level. If you have PTF2 or later, there is no need to perform this.

When a partition is switched between LPAR and SMP (Single Machine Partition) mode.

When a partition is redefined, i.e. It could be assigned a new partition ID.

When a partition is upgraded, installed with a new level of AIX.

When hostnames are swapped between 2 partitions.

Step 1: Removing IBM.ManagedNode Resources on HMC

On HMC, execute these commands:

> /usr/sbin/rsct/bin/rmrsrc  -s "Hostname!=’t’" IBM.ManagedNode
  > /usr/sbin/rsct/bin/rmcctrl -z
  > /usr/sbin/rsct/bin/rmcctrl -Z

Step 2: Removing IBM.ManagementServer Resource on Partitions

As documented in the IBM Hardware Management Console for pSeries Operations Guide. Service Focal Point, section Getting Started, the following procedure is to be performed on the affected partitions:

> /usr/sbin/rsct/bin/rmrsrc  -s "Name!=’t’" IBM.ManagementServer
  > /usr/sbin/rsct/bin/rmcctrl -z
  > /usr/sbin/rsct/bin/rmcctrl -A

Wait for a few minutes, then checking for IBM.ManagementServer resource(s) by

> lsrsrc IBM.ManagementServer

Resource Persistent Attributes for IBM.ManagementServer
  resource 1:

Name		= " hmc.yourcompany.com "
  Hostname		= " hmc.yourcompany.com "
  ManagerType	= " HSC "
  LocalHostname	= " par_01.company.com "
  NodeNameList	= {"par_01.company.com"}

Ÿ Verify$N)N*N,NcN¡NüN

OO

| O*O4O5OwOxOŽOžO¤O¦O§OÈOÉOÔOÕO | PPP{P¦P§P¨PuQxQzQ{QŠQ‹Q“Q#R$R1R2RëSøSùSöTùTýTUWWWæWôWõWüúüüüüüüøøøøøøøøüúüüøøøüøøøøøøøøøøøøøøøüøøøøøøøøõóóóõøøøøøøøøøøððîîîîêóóóóèåèóóããbU�^^]cU�bc(V�V�MM]M^YõWùWúWXXX XXU�1GHIJWX™ÆÇÈñi | j | Œ | Ž | � | ­ | ¯ | ° | â | ä | å | RTúôôôôôôôôôôôôôôôôëÚ×ÔÈ×ÔÈÅÔÈÅÔÈ×Ô X¸¹¾ÿ$Ÿ*On/ | X¸¹¾ÿ$Ÿ*'" # I L M ¦  € ¿ Â Ã |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

@

C

D

–

™

š

Ì

Ï

Ð

B

E

F

¢

¥

¦

ß

â

ã

GJóðíóêíóðíóðíóðíóðíóðíóêíóðíóðíóðíóðíóðí
X¸¹¾ÿ$Ÿ*'JK^abqtu“äåæí

óðíóðíóÍ­­ªŠŠnhbR/R/X¸l¹¾(£ƒ	V		

	


	

	R

4XX/

4/

| 4Ð.0O |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |